## Slide 1
Vision-Based Precision Pose Estimation
Autonomous Formation Flying
Machine Learning Mini-Project | UE24CS352A
Shashank D — PES1UG24CS433
Shriya K — PES1UG24CS448
1

## Slide 2
Problem Statement
Estimate the relative pose of a leader aircraft from observations obtained by a follower aircraft's monocular camera.
Pose variables considered in the discrete estimator: relative X, Y, Z position and roll.
The system combines learned coarse estimation with model-based geometric refinement.
2

## Slide 3
Reference Approach and Motivation
Reference approach: structural feature measurements → ANN pose classification → particle-filter refinement.
The ANN provides a fast but discrete pose estimate over 4,800 pose classes.
Particle filtering incorporates motion and feature-reprojection likelihood, but is computationally expensive.
Our extension adds continuous geometric refinement using Perspective-n-Point (PnP).
3

## Slide 4
Proposed System Pipeline
Synthetic
Aircraft
Gimbaled
Camera
14 × 2D
Keypoints
42-D
Features
ANN
Classifier
Particle
Filter
PnP
Refinement
Final
Pose
Core idea: ANN supplies a coarse estimate; PnP converts 2D–3D correspondences into a continuous pose refinement.
4

## Slide 5
Synthetic Dataset and Feature Representation
14 predefined aircraft structural keypoints are projected into the camera image.
Each keypoint contributes (u, v, occlusion), giving 14 × 3 = 42 input features.
The pose space is discretized into 10 X bins × 10 Y bins × 8 Z bins × 6 roll bins = 4,800 classes.
Synthetic projection includes camera geometry, visibility/occlusion checks, and pixel noise.
5

## Slide 6
ANN Pose Classifier
Input: 42-dimensional feature vector.
Architecture: 42 → 100 → 100 → 4,800.
Activation: ReLU.
Output: 4,800-way softmax pose classification.
Training: cross-entropy loss with Adam optimization.
42
100
100
4800
6

## Slide 7
Particle Filter
Initialize particles around the ANN-derived pose estimate.
Propagate particles using the simulated relative-motion model.
Project aircraft keypoints for each particle.
Weight particles using feature reprojection error.
Resample particles according to their likelihood.
The benchmark shows that PF improves some pose components but increases overall positional RMSE in this setup.
7

## Slide 8
PnP Refinement: Proposed Extension
Use known 3D aircraft keypoints and detected 2D image correspondences.
Warm-start PnP from the coarse pose.
Apply OpenCV iterative solvePnP refinement.
Convert the optimized camera-frame solution back to the follower-body frame.
Output: continuous 6-DOF pose estimate; the current benchmark reports position and roll metrics.
8

## Slide 9
Quantitative Benchmark Results
10-second formation-flight trajectory, 100 steps at 10 Hz
Method | Pos RMSE (m) | Pos Median (m) | Pos Max (m) | Roll RMSE (°) | Latency (ms) | FPS
ANN | 22.549 | 17.402 | 40.342 | 10.75 | 0.50 | 1986.4
ANN + PF | 24.469 | 23.865 | 36.943 | 3.26 | 220.41 | 4.5
ANN + PnP | 0.644 | 0.380 | 1.888 | 0.54 | 0.41 | 2416.9
PnP provides the strongest continuous-pose result in the current simulated benchmark.
The benchmark assumes a gimbaled camera whose orientation tracks the target line of sight; this simulation assumption should be stated explicitly.
9

## Slide 10
Conclusion and Future Work
ANN provides a fast coarse pose estimate over a large discrete pose space.
Particle filtering adds temporal/model-based refinement but has high computational cost.
PnP provides a low-latency geometric refinement from 2D–3D correspondences.
Current system starts from structural feature measurements rather than raw-image feature detection.
Future work: raw-image keypoint detection, real flight imagery, robust outlier rejection, uncertainty estimation, and bundle adjustment.
10